## Slide 1: Hazardous Waste Compatibility
- Jesus Hernandez

## Slide 2: Hazardous Waste Storage Compatibility
Compatible storage minimizes danger
Follow accumulation regulations
Separate streams by compatibility
Additional information concerning compatibility can be found in StaO 5090.5D (Hazardous Waste Management).

## Slide 3: Container Separation
Separate containers holding incompatible hazardous waste by:
  Berm
  Dike
  Wall
  Similar device
Hazardous waste and hazardous material must never be stored together!

## Slide 4: Chemical Compatibility Charts
Two different chemical compatibility charts
Resource Conservation and Recovery Act (RCRA) Chemical Waste Compatibility List
  Arranges chemicals into 12 categories (1-A through 6-A and 1-B through 6-B)
  Describes potential hazards of interactions between categories
Environmental Protection Agency (EPA) Chemical Compatibility Chart
  Arranges hundreds of chemicals into 41 reactionary groups (organic acids, ethers, caustics, etc.)
  Charts potential reactions between each binary combination of reactionary group

## Slide 5: RCRA Compatibility
1-A + 1-B = Heat generation; violent reaction
2-A + 2-B = Fire or explosion; flammable hydrogen gas
3-A + 3-B = Fire, explosion, or heat generation; flammable or toxic gases
4-A + 4-B = Fire, explosion, or violent reaction
5-A + 5-B = Toxic hydrogen cyanide or hydrogen sulfide gas
6-A + 6-B = Fire, explosion, or violent reaction

## Slide 6: EPA HW Compatibility Chart

## Slide 8: Summary
Storing incompatible wastes together can result in severe hazards and could cause damage to the environment, injury, or death.
Incompatibility charts will allow you to store hazardous waste safely if you know how to use them correctly
Incompatible wastes must be separated by a berm, dike, wall, or similar device.