## Slide 1: Consolidated Emergency Response/Contingency (CERC) Plan Training
Section 1
Hazardous Material (HM) &
Hazardous Waste (HW) Handling
Please print and sign your name on the training roster.
Persons Trained: Hazardous Materials/Waste Handlers/ECCs (Annual Training Requirement)

## Slide 2: LEARNING OBJECTIVES
Enabling Learning Objectives:
  Identify unit’s HM/HW.
  Locate unit’s SDS Binder.
  Know the difference between HM and HW
  Safely handle and store HM/HW.
  Describe HM/HW recordkeeping needs.
Terminal Learning Objective: Meet the Consolidated Emergency Response/Contingency Plan annual training requirement for hazardous material and hazardous waste training.

## Slide 3: BACKGROUND
We use hazardous materials (HM) daily in maintenance, repair, and cleaning activities.
Some HM processes result in hazardous waste (HW) being generated (used oil, waste paint, used batteries, etc.).

## Slide 4: UNIT RESPONSIBILITIES
Develop and implement a written plan and procedures for HM/HW management that meets requirements of MCO 5090.2, StaO 5090.5C, Station Safety Office, and Environmental Department policies.
Comply with applicable Federal, State, and local laws and regulations applicable to HM management and the safety and health of HW operations.
Establish procedures to control, track, and reduce the variety and quantities of HM in use, in storage or stocked, and disposed of as HW.

## Slide 5: REGULATIONS
Protecting workers that handle hazardous material.
  OSHA, 29CFR
  MCO 5100.29B
  StaO 5100.8

## Slide 6
Protecting workers and the environment from the hazardous wastes generated. Requires annual training for workers handling HM or HW.
  EPA, 40 CFR
  California Health and Safety Code Division 20
  Title 22 California Code of Regulations Division 4.5
  MCO 5090.2 Environmental Compliance Manual
  Hazardous Waste Management Plan, StaO 5090.5_
REGULATIONS

## Slide 7: HAZARDOUS MATERIALS
Hazardous Materials (HM): chemical products that, because of their toxicity or chemical properties, pose physical or health risks to humans or to our environment.
HM is good, unused, uncontaminated material:
  POL’s (hydraulic fluid, oil, JP-5/8, diesel fuel)
  Batteries of any type
  Detergents & Cleaners
  Aerosols (any type)
  Paints & Solvents
  Gasoline
  Adhesives

## Slide 8
AUTHORIZED USE LIST (AUL)
For our safety and environmental compliance the HM we use must be screened and inventoried on the “AUL”
  AUL is a management tool and inventory of a unit’s HM.
  HM on the AUL must be approved by Station Safety, the Industrial Hygienist, and Environmental Department.
  HM is easily procured from the HazMinCtr.
  Unit on-hand quantities of HM are limited to a one week’s supply although exceptions can be approved by Safety.
Contact Station Safety for AUL assistance.

## Slide 9: SAFETY DATA SHEETS (SDS)
Hazard Communication Standard requirement to provide a safe workplace to HM users:
  Provides detailed HM information, first aid, response.
  Required for each chemical in the workplace.
  Must be readily available at all times.
  Must be read before working with the HM.
Unit’s SDS’s are located __________.
Copies available through HMMS or HazMinCtr.

## Slide 10: CONTAINER LABELS
HM needs to be labeled:
  Manufacturer’s name, address, and emergency phone number
  Common chemical name
  Identify the hazard(s) in English
  Appropriate hazard warnings (words, DoT labels or placards, NFPA Diamond, HMIS label, etc.)
DD FORM 2522 can replace the manufacturer’s label if it needs to be replaced.

## Slide 11: HM PROCUREMENT
HM is procured from the HazMinCtr.
HM must be approved on unit’s AUL by Safety, Industrial Hygiene, and Environmental.
Hazardous Waste Coordinator procures HM with a request through Supply/S-4 then to HazMinCtr.
HM is picked up from the HazMinCtr or can be delivered.
HM hand-on stock limited to a 7-day supply.

## Slide 12: HM HANDLING
Read the SDS and label for HM hazards.
Wear Personal Protective Equipment (PPE).
Ensure there is adequate ventilation (natural or mechanical).
Use funnels, drip pans, pads, and shop towels when pouring HM.
Attach grounding and bonding wires when pouring and storing flammable liquids.

## Slide 13: HM STORAGE
Chemical compatibility (refer to SDS).
  Don’t store corrosives with flammables
  Don’t store flammables with oxidizers
Flammables in flammable lockers.
Rotate stock and use within shelf-life:
  Check shelf-life when new HM is received
  Use the older HM first
Secondary containment.
  Flammable Storage Lockers
  Bermed areas

## Slide 14
HAZARDOUS WASTE
Hazardous Waste (HW) is HM we’re going to dispose because it’s used, spent, or no good:
  Used oil or POL (oil, hydraulic fluid, JP-5/8, diesel fuel)
  Aerosol cans
  Paint chips w/lead or chromates
  Spent toxic or flammable solvents
  Used batteries of any type (alkaline, lithium, mercury, etc.)
  Past shelf-life (expired) HM
  Spent fluorescent light bulbs
  Spilled HM contaminated debris
We cannot dispose of HM/HW in the trash or recycling bins!

## Slide 15: HW MANAGEMENT
HW is managed per Environmental Department’s Hazardous Waste Management Plan (HWMP- StaO 5090.5_).
HWMP is written to maintain compliance with applicable Federal, State, County of San Diego, USMC HW regulations.
Waste Protocol Sheets (HWMP Chapter 14) lists each “waste stream” with easily referenced waste management guidance:
  Defines the waste stream.
  Provides container (drum, bucket, box, pallet, etc.) selection information.
  Tells how to correctly fill out the waste’s container label.
  Gives the waste’s accumulation time limit.
  Provides waste disposal information.

## Slide 16: HW HANDLING
Use appropriate Personal Protective Equipment:
  Gloves, Goggles, Face Shield, Rubber Apron.
Use funnels, drip pans, pads, shop towels, and a buddy when pouring HM/HW to minimize spillage and clean ups.
Use grounding straps when storing ignitable waste and bonding straps when pouring liquids.
Do not mix waste streams.
Contact unit’s HWC for guidance for disposal procedures.

## Slide 17: HW ACCUMULATION
Waste Accumulation Site
  Controlled area (usually fenced and bermed containment cells or fabricated storage shed) used to accumulate regulated waste.
  Lids and labels on containers.
  No signs of spillage.
  Inspected weekly (ASTs containing HWs inspected daily); records maintained for 3 years.

## Slide 18: HW Accumulation (2 of 2)
Satellite Accumulation Site
  At or near the point of generation (paint shop, battery shop, hangar deck, admin office, etc.).
  Up to 55-gallons TOTAL HW, not per waste stream. MCO 5090.2.
  Container must be labeled, closed when not in use, and under the control of the operator.
  Waste is disposed of when:
    the container is full,
    55 gallons is reached, or
    within nine months, whichever occurs first.
  Must be approved by Miramar FD and EMD, also identified on the unit’s Consolidated Emergency Response/Contingency Plan Map.

## Slide 19
HW MINIMIZATION
Minimize waste at the source:
  Use only authorized hazardous materials.
  Order what you need and use it properly.
  Keep lids secured when not adding or removing HW.
  All containers must be labeled.
  Don’t mix waste streams.
  Use funnels, drip pans, shop towels, and reusable pads.
  Handle HM and HW carefully to reduce spills.
Recycle or Reuse:
  Return unwanted HM to the HazMinCtr.
  Recycle plastic and metal containers.

## Slide 20: RECORDKEEPING & REPORTING
Consolidated Emergency Response/ Contingency Plan
  Issued by SD County through Environmental Dept.
  Four parts: Inventory, Spill Plan, Training, Spill Equipment.
Contingency Plan Training Rosters
  CERC annual training required for personnel involved in HM/HW operations.
  Maintained roster in binder II.
Unified Program Facility Permit
  Issued by San Diego County Dept. of Env. Health.
  Applied for and renewed by the EMD.

## Slide 21: Recordkeeping & Reporting (2 of 3)
NOTE: All records are legal documents that must be maintained for at least three years.
Waste Disposal Records:
  Copies of disposal receipts
  HW Transfer Log Books (transferred to HazMinCtr/unit)
Unit’s Spill Log:
  Records unit’s spills, clean-ups, and storm water releases from secondary containment.

## Slide 22: Recordkeeping & Reporting (3 of 3)
AUL (updates)
  Make additions/deletions with Station Safety
  Procure from the HazMinCtr
  (not Serv-Mart, MCX, Lowe’s, Home Depot, etc.)
Aerospace Coatings List (coatings applied to aircraft)
  Issued by Environmental Dept’s Air Quality Engineer
  Submit Usage Reports to Air Quality Engineer
Air Quality Permits (parts washers, paint booths, test cell, etc.)
  Comply with permit conditions

## Slide 23: REVIEW
Identify HM needs and establish a unit AUL through Station Safety, IH, and Environmental Dept.
Have SDS’s on-hand or readily available.
Ensure all personnel use PPE for specific chemical hazards.
Identify waste streams and ensure personnel know how to containerize, label, and dispose of HW.
Maintain records for HM usage, HW disposal, site inspections, and training.
Please sign-in on today’s Training Roster.

## Slide 24: QUESTIONS?
Contact your unit’s Hazardous Waste Coordinator (HWC) or your Group’s Environmental Compliance Coordinator (ECC) for environmental assistance.
Unit and Group ECCs should contact the Environmental Department’s Waste Management Division at 307-1108 for questions regarding this presentation and/or for training assistance.